## Slide 1: Physical Layer Network Coding in Two-Way Relaying Systems
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAAAA
Dirk Wübben, Yidong Lang, Meng Wu, Armin Dekorsy
Sino-German Workshop, 04/03/14 - 07/03/14, Shenzhen

## Slide 2: Research in a nutshell
Compressed Sensing Carsten Bockelmann
CS-MUD
Joint data and activity detection
Distributed CS
Projects:
  DFG: NiCoM, CoSeM, INNS
  EU: METIS
Applications: Massive M2M communication , invasive neuronal signal recording
Publications (2012-2013): ETT Journal, 9 conferences
In-Network-Processing Henning Paul
Distributed linear and non-linear estimation
Consensus-based estimation and detection (DICE-Algo)
Projects:
  Uni-Bremen
  EU: iJoin
Applications: Environmental monitoring, 5G -ultra dense networks (small cells)
Publications (2012-1013): IEEE Letter, 6 conferences
Cooperative Communications Dirk Wübben
Network coding
Two-way-relaying, multi-hop-relaying (IDMA)
Waveform design
Projects:
  DFG: COINII, COINIII
  EU: METIS, iJoin
  Industry
Applications: 5G: D2D, relaying networks, ultra-dense networks
Publications (2012-2013): 1 book chapter, 2 journals, 11 conferences

## Slide 3: Overview
Two-Way-Relay system with Physical Layer Network Coding
Channel Decoding and Physical Layer Network Coding schemes
  Separate Channel Decoding (SDC)
  Joint Channel decoding and physical layer Network Coding (JCNC)
  Generalized JCNC (G-JCNC)
  Simulation results
Implementation aspects
  Hardware testbed
  Carrier Frequency Offset analysis

## Slide 4: Introduction
Two-Way-Relaying system: Two sources A and B exchange information assisted by a relay R
Assumptions:
  Half-duplex constraint: no simultaneous transmission and reception
  No direct communication link between A and B
Relay processing:
  Processing at relay is crucial for end-to-end performance
  Physical layer network coding (PLNC) to combine both received signals
Objective: Design of joint decoding and PLNC schemes at relay

## Slide 5: Physical Layer Network Coding
A and B use same code  (e.g. LDPC) with cA and cB as codewords
M: modulation scheme
A and B transmit simultaneously to R
R estimates relay codeword AB using superimposed signal yR
Phase l (Multiple access)
Phase ll (Broadcast)
Challenge: How to estimate AB from yR ?
  Joint channel decoding and PLNC
  Separated channel decoding (SCD)
  Joint channel decoding and physical layer network coding (JCNC)
  Generalized JCNC (G-JCNC)

## Slide 6: Some definitions (examplary for BPSK, M=2)
Decoding acts on superimposed noise-free receive signal
BPSK with xA, xB {}: sAB has at most M2 =4 constellation points (hypotheses) with sAB SAB and SAB as set of hypotheses
Define code symbol tuple cAB = [cA cB] CAB
A-posteriori probability (APP) of i-th hypothesis with i=0..3
Mapping:
i | cA | cB | cAB | cAB | xA | xB | sAB
0 | 0 | 0 | 0 | 0 | 1 | 1 | hA+hB
1 | 1 | 0 | 1 | 1 | -1 | 1 | - hA+hB
2 | 0 | 1 | 1 | D | 1 | -1 | hA-hB
3 | 1 | 1 | 0 | 1+D | -1 | -1 | -hA-hB


## Slide 7: Separated Channel Decoding (SCD)
Idea: Estimate code symbols cA and cB explicitly and apply succeeding XOR operation to obtain AB
  Calculate APPs for cA and cB
  Perform symbolwise decoding for each source by sum-product algorithm (SPA)
Interpretation as common multiple access problem (counterpart is processed as interference)
e.g. for cA
Parallel SCD (P-SCD)
Serial SCD (S-SCD): cancel interference caused by A for B

## Slide 8: Joint Channel Decoding and Physical Layer Network Coding (JCNC)
Idea: If we assume code  to be linear then AB= cA  cB is a valid codeword
 Perform decoding of codeword AB without explicitly decoding cA and cB
  Calculate APPs for codesymbol cAB
  Perform symbolwise decoding for cAB using SPA

## Slide 9: Generalized JCNC (G-JCNC)
Idea: Perform decoding on hypotheses for combined code symbols cAB = [cA cB] CAB with succeeding mapping on AB  jointly decode two codes by a generalized Sum-Product Algorithm (G-SPA)
G-SPA: decodes code symbol tuples cAB = [cA cB]T
  Combining code symbols [cA cB]T  leads to new code with codewords of size 2xN defined by parity-check equation
  Binary parity-check matrix H of code   we can use factor graph of code 
  Decoder calculates APPs for each codesymbol cAB
PLNC mapping: Mapping of codesymbol cAB with maximum APP to XOR symbol AB
We can alternatively represent code symbol tuples cAB = [cA cB]T by quaternary symbols cAB   decoder over

## Slide 10: Generalized JCNC (G-JCNC)
Receiver block for G-JCNC
Generalized SPA for
PLNC mapping
G-SPA4 delivers APP vector for each cAB
PLNC mapping rule (BPSK)
AB

## Slide 11: Ambiguity of constellation points/hypotheses
LDPC with code length N=1000, Rc=0.4, 10 iterations per SPA, hA=1 and hB=, fixed Eb/N0 = 3 dB
SCD very sensitive due to problem of ambiguity
JCNC robust but generally shows low performance
G-JCNC quite robust and always shows best performance
(AWGN)

## Slide 12: LLR-Distributions
Diverse channel coefficients (hA and hB ) are advantageous to SCD
Additional antenna (J=2) at relay does not change relation
OFDM: Fro each subcarrier we receive different signal constellations
LDPC, 1024 subcarrier, QPSK, SNR = 5 dB

## Slide 13: FER at relay for OFDM
LDPC, each OFDM symbol individually encoded, 1024 carriers, 100 iterations per SPA, single antenna relay
G-JCNC outperforms all other schemes
SCD better than JCNC
Claims also valid for other code rates

## Slide 14: Hardware Plattform
Real time implementation of basic LTE Rel8 Downlink phy-layer processing
Objective: test of different decoding schemes (SCD, JCNC, GJCNC) with carrier-frequency-offset (CFO) impairments
source A
source B
relay

## Slide 15: Carrier Frequency Offset (CFO) analysis: Test-bed results
BER measured at relay
Performance loss with increasing CFO difference
Measured performances confirm simulation results  G-JCNC with best performance
normalized CFO ²i= ¢fiTS, with i = A,B
¢fi: carrier offset, TS : OFDM symbol duration

## Slide 16: Further research activities on relaying
5G: EU-Project METIS
Mobile and wireless communications Enablers for the Twenty-Twenty (2020) Information Society
Bi-directional Relaying with non-orthogonal medium access
Two-way relaying with multiple flows and multiple communication pairs
Application of Interleave Division Multiple Access (IDMA) as non-orthogonal medium access
Conceptual design studying rate adaptation and power allocation and the design of transmitter and receiving schemes

## Slide 17: Further research activities on relaying
Research project with University of Rostock
Joint Optimization of Generalized Multicarrier Waveforms and Power Allocation for Two-Way Relay Systems
Coded Filter Bank Multicarrier (cFBMC) for two-way relay system
Derivation of two-way relay MAC-system model
Design of novel cFBMC receiver concepts to estimate common relay message
Development of joint impulse shaping and power allocation strategies
System design with high scalability for balancing complexity & performance

## Slide 18
Thank you very much for your attention!

## Slide 19: References
D. Wübben: Joint Channel Decoding and Physical-Layer Network Coding in Two-Way QPSK Relay Systems by a Generalized Sum-Product Algorithm, ISWCS 2010, York, UK, Sept. 2010
D. Wübben, Y. Lang: Generalized Sum-Product Algorithm for Joint Channel Decoding and Physical-Layer Network Coding in Two-Way Relay Systems, GLOBECOM 2010, Miami, USA, Dec. 2010
M. Wu, D. Wübben, A. Dekorsy: Mutual Information Based Analysis for Physical-Layer Network Coding with Optimal Phase Control, SCC 2013, Munich, Germany, Jan. 2013
M. Wu, D. Wübben, A. Dekorsy: Physical-Layer Network Coding in Coded OFDM Systems with Multiple-Antenna Relay, VTC 2013-Spring, Dresden, Germany, Jun. 2013
F. Lenkeit, C. Bockelmann, D. Wübben, A. Dekorsy: IRA Code Design for IDMA-based Multi-Pair Bidirectional Relaying Systems, BWA 2013, GLOBECOM Workshop, Atlanta, USA, Dec. 2013
M. Wu, F. Ludwig, M. Woltering, D. Wübben, A. Dekorsy, S. Paul: Analysis and Implementation for Physical-Layer Network Coding with Carrier Frequency Offset, WSA 2014, Erlangen, Germany, Mar. 2014 (accepted)
D. Wübben, M. Wu, A. Dekorsy: Physical-Layer Network Coding with Multiple-Antenna Relays, Chapter in MIMO Processing for 4G and Beyond: Fundamentals and Evolution, CRC Press, Apr. 2014

## Slide 20: Backup

## Slide 21: CFO analysis: Simulation results
No CFO
CFO with ICIC
G-JCNC outperforms other coding schemes
G-JCNC achieves almost performance of CFO-free case if ICIC is applied
CFO  Inter-Carrier Interference
Techniques applied: CFO compensation and Inter Carrier Interference Cancellation (ICIC)

## Slide 22: Ambiguity of constellation points/hypotheses
i | cA | cB | cAB | cAB | sAB
0 | 0 | 0 | 0 | 0 | 2
1 | 1 | 0 | 1 | 1 | 0
2 | 0 | 1 | 1 | D | 0
3 | 1 | 1 | 0 | 1+D | -2
SCD: sAB=0  ambiguity for cA and cB
JCNC: sAB=0 ) AB =1 and sAB {}: ) AB =1  no ambiguity
G-JCNC: 3 hypotheses to decode for 4 code symbols cAB  ambiguity
SCD and GJCNC: no ambiguity  performance improvement
JCNC: reduced Euclidian distance  performance loss
(AWGN)
: four constellation points

## Slide 23: Testbed set-up: OFDM transmission
Define: normalized CFO ²i= ¢fiTS, with i = A,B

## Slide 24: Testbed set-up
Flexible hardware solution
Baseband processing can be partitioned in DSPs and FPGAs
RF transceivers for 2.4 GHz and 5 GHz ISM bands

## Slide 25: End-to-End BER: Normalized Block Fading Channels
Parameters:
LDPC with code length N=1000, Rc=0.4
10 iterations per SPA
Normalized block fading channel hA=1 and hB= with Á  U(- ¼, ¼)
Received signal points may overlay
P-SCD and S-SCD perform worst
Improved performance by JCNC
G-JCNC outperforms common approaches significantly ( 1dB gain at BER 10-5)

## Slide 26: Summary
Physical Layer Network Coding (PLNC) requires only 2 transmission steps
Generalized Joint Channel Decoding and Physical Layer Network Coding (G-JCNC)
  Generalized Sum-Product Algorithm over performs joint decoding of both channel codes
  Strong performance improvements and robustness
  Generalization for higher order modulation
Practical aspects, e.g., Carrier Frequency Offset (CFO)
  Introduces Inter Carrier Interference (ICI)
  ICI cancelation (ICIC) with modified S-SCD and G-JCNC results in only small performance degradation with moderate CFO

## Slide 27: Two-Way-Relaying: System Model

## Slide 28: Current Investigations
Extension to multiple-antenna relays and distributed relays
Investigation of implementation cost and efficient hardware
Proof of concept by real-time testbed
Realization aspects, e.g., carrier frequency offset (CFO)
Joint DFG project with Institute for Electrodynamics and Microelectronics:
Physical Layer Network Coding in Two-Way Relaying Systems with Multiple-Antenna Relays or Distributed Single-Antenna Relays