## Slide 1: Lattice Partition Based Physical-layer Network Coding
Qifu (Tyler) Sun
University of Science and Technology Beijing
6, Mar, 2014 @ Sino-German Workshop
Notes: Thanks Yonghui. Good afternoon everyone. It’s my greatest pleasure to have a visit at the University of Sydney. It’s also my first time to come to the Southern Hemisphere. So I’m so pleasant to have a chance to experience a sunny shiny X’mas.
Now more precisely, besides INC, I’m also affiliated with the INC Shenzhen branch. INC branch was just established at the beginning of this year. Its goal is to establish a tighter connection and collaboration with research institutes and industries in mainland China. In particular, via this newly established branch, we are able to apply for various types of research grants supported by different tiers’ government in mainland China.
OK. Today’s talk …
Perhaps LNC, you may not hear about this term.
However, for another concept that is closely related to it, called Physical layer network coding, it may not be so unfamiliar to you any more.

## Slide 2: References
  B. Nazer and M. Gastpar, “Reliable physical layer network coding,” Proceedings of the IEEE, vol. 99, no. 3, Mar., 2011.
  C. Feng, D. Silva, and F. R. Kschischang, “An algebraic approach to physical-layer network coding,” IEEE Transactions on Information Theory, vol. 59, pp. 7576-7596, no. 11, Nov. 2013.
  Q. T. Sun, J. Yuan, T. Huang and W. K. Shum, “Lattice network codes based on Eisenstein integers,” IEEE Transactions on Communications, vol. 61, no. 7, Jul., 2013.

## Slide 3: Physical-layer Network Coding (PNC)
  Relay computes the modulo-two sum wAwB from linearly superimposed receiving signals yR= xA+xB
  Enhances the throughput of a binary-input TWRC.
  [Nam-Chung-Lee’10]roach the capacity upper bound of a Gaus
Zhang-Liew-Lam, Hot topic: physical layer network coding, MobiCom, 2006.
Popviski-Yomo, The anti-packets can increase the achievable throughput of a wireless multi-hop network, ICC, 2006.
Nazer-Gastpar, ,Computing over multiple-access channels with connections to wireless network coding, ISIT, 2006..
F
C
yR= xA+xB

## Slide 4: Physical-layer Network Coding (PNC)
  Relay computes the F-linear combination of aAwA+aBwB from linearly superimposed receiving signals yR= hAxA+ hBxB
  [Nam-Chung-Lee’10]roach the capacity upper bound of a Gaus
We need an appropriate modulation scheme to map linearity from over complex number field to over finite fields.
aAwA+aBwB
yR= hAxA+ hBxB

## Slide 5: Physical-layer Network Coding (PNC)
  Relay computes the F-linear combination of aAwA+aBwB from linearly superimposed receiving signals yR= hAxA+ hBxB + z
  [Nam-Chung-Lee’10]roach the capacity upper bound of a Gaus
We need an appropriate modulation scheme to map linearity from over complex number field to over finite fields.
We need an appropriate coding technique for reliable PNC over F.
aAwA+aBwB
yR= hAxA+hBxB+z
  Good candidate: Lattice partition structure embedded in C

## Slide 6: Lattice Partitions in C
  Why is lattice partition a good candidate to model PNC?
  Based on lattice partition structure,
  the arithmetic of finite field can be appropriately represented over complex plane.
  several capacity-achieving lattice codes have been designed for (complex) Gaussian channels.
  C = log2(1 + |h|2 SNR) (bits / channel use)

## Slide 7: Almost capacity-achieving PNC in TWRC
  RA  log2(1 + |hA|2 SNR), RB  log2(1 + |hB|2 SNR).
  // operates half duplex mode;
  // downlink transmission is not the bottleneck;
  // over complex channels.
yR= hAxA+ hBxB

## Slide 8: Almost capacity-achieving PNC in TWRC
  RA  log2(1 + |hA|2 SNR), RB  log2(1 + |hB|2 SNR).
  [Nam-Chung-Lee’10] By adaptation of capacity-achieving lattice codes for Gaussian channels to PNC,
  RA = log2( + |hA|2 SNR), RB = log2( + |hB|2 SNR)
  Lattice partition based PNC approaches the capacity upper bound of a Gaussian TWRC within 1/2 bits.
yR= hAxA+ hBxB
  // hA, hB known at A and B

## Slide 9: CF: Lattice partition based PNC in MARC
q-ary input
Nazer-Gastpar, Compute-and-Forward: Harnessing Interference through Structured Codes, IEEE Trans. Inform. Theory, 2011.
Multi-user
Fading hlC
Gaussian Multiple Access Relay Channel
Notes: a complex circularly-symmetric additive white Gaussian noise

## Slide 10: CF: Lattice partition based PNC in MARC
Nazer-Gastpar, Compute-and-Forward: Harnessing Interference through Structured Codes, IEEE Trans. Inform. Theory, 2011.
q-ary input
Multi-user
Fading hlC
Key idea:
Based on y, relay decodes a linear function of wi w.r.t. a coefficient vector a, instead of decoding each wi individually.
Gaussian Multiple Access Relay Channel

## Slide 11: CF: Lattice partition based PNC in MARC
The CF scheme is proposed based on an infinite sequence of good lattice partitions over Cn, which can asymptotically achieve the computation rate
// Computation rate = Reliable transmission rate of u
  // h not known at transmitters
Notes: … such that under this rate the relay can decode the desired linear combination u with arbitrarily small error.
Here the information of fading is supposed to be known at the relay but not the transmitters.

## Slide 12: CF: Lattice partition based PNC in MARC
The CF scheme is proposed based on an infinite sequence of good lattice partitions over Cn, which can asymptotically achieve the computation rate
// This scheme is not practical to implement. // An information theoretical guideline

## Slide 13: Lattice Network Coding (LNC)  An algebraic framework for practical design
Feng-Silva-Kschischang, An algebraic approach to physical-layer network coding, IEEE Trans. Inform. Theory, 2013.
  Considers finite dimensional lattice partitions for PNC.
  Makes direct connection between the LNC design and module theory over principal ideal domains in commutative algebra.
Notes: In order to design and implement practical CF schemes, most recently, an algebraic framework, called lattice network coding, was proposed by Feng-Silva-Kschischang.
The system model for LNC is same as the one for Compute-and-Forward

## Slide 14: Message space of LNC
  Let R  C be a principal ideal domain (e.g., Z, Z[i] := Z+iZ)
  An n-dim R-lattice  is a subset of Cn that is closed under ‘+’ and ‘ by scalars in R’. // an R-module
  Given a sublattice  of ,
  the quotient group / naturally forms a lattice partition of . // an R-module
   = Z
0
3
–3
3Z
1+3Z
2+3Z
   = 3Z
  / = Z/3Z  F3
: fine lattice; : coarse lattice

## Slide 15: Message space of LNC
  Let R  C be a principal ideal domain (e.g., Z, Z[i] := Z+iZ)
  An n-dim R-lattice  is a subset of Cn that is closed under ‘+’ and ‘ by scalars in R’. // an R-module
  Given a sublattice  of ,
  the quotient group / naturally forms a lattice partition of . // an R-module
  The message space of an LNC W = /
wl is a coset in /

## Slide 16: Message space of LNC
  Let R  C be a principal ideal domain (e.g., Z, Z[i] := Z+iZ)
  An n-dim R-lattice  is a subset of Cn that is closed under ‘+’ and ‘ by scalars in R’. // an R-module
  Given a sublattice  of ,
  the quotient group / naturally forms a lattice partition of . // an R-module
  The message space of an LNC W = /
Code Rate
=
log2|/|

## Slide 17: Message space of LNC over Z[i]
  The set of Gaussian integers Z[i]  C forms a PID.
    Z[i] = {a  1+b  i : a, b  Z}
     = Z[i],  = (1+i)Z[i], / = F2 = {■ ■}
    F2 = Z[i]/(1+i)Z[i] = Z/2Z
1
i

## Slide 18: Message space of LNC over Z[]
  E.g., the set of Eisenstein integers Z[]  C forms a PID.
    Z[] = {a  1+b   : a, b  Z},  =
     = Z[],  = 2Z[], / = F4 = {■ ■ ■ ■}

1
W = (Z[]/2Z[])n :
Baseline (uncoded) LNC

## Slide 19: Encoding of LNC
  The encoding function E maps each coset wl  W = / to a coset leader xl  wl, which is in the fundamental Voronoi region V() of .
Z[]/2Z[], / = F4

## Slide 20: Decoding of LNC at the relay
  Received signal vector , hl  C
  Relay’s goal: based on y, decode , al  R
  The real message decoded is û = (D(y))
Notes:   Now let’s move from the encoding side to the decoding side. After the L source signals transmitted through the Gaussian MAC, the received signal vector is a linear combination of x w.r.t. the fading gains, plus a vector z representing the complex circularly-symmetric Additive White Gaussian Noise.
  The goal of the relay is to decode an R-linear combination of source messages

## Slide 21: Decoding function
  û = (D(y))
natural projection from  onto /
quantizer: map to a closest lattice point in 
     = Z[],  = 2Z[], / = F4 = {■ ■ ■ ■}
y
Notes: The physical meaning of the decoding function is as follows.
First the quantizer D will map the scaled version of received signal y to a closest fine lattice point, and then project this fine lattice point to the coset in the lattice partition it belongs to. Recall that every message in the message space corresponds to a coset in the lattice partition.

## Slide 22: Decoding error
  Received signal vector
  Relay’s goal: based on y, decode , al  R
  The real message decoded is û = (D(y))
  A decoding error occurs when u  û.
effective noise n
Non-trivial analysis

## Slide 23: Decoding error probability of LNC
  [Feng-Silva-Kschischang] Consider an LNC / with  hypercube shaped, i.e., equivalent to Z[i]n.
Notes: Here, the shape of the sublattice Lambda’ is assumed to be isomorphic to a hypercube after possible rotation, reflection and multiplication by a scaling factor.

## Slide 24: Decoding error probability of LNC
  [Feng-Silva-Kschischang] Consider an LNC / with  hypercube shaped, i.e., equivalent to Z[i]n. The union bound Estimation (UBE) of the decoding error probability for / is
  d(Λ/Λ) = minimum inter-coset (Euclidean) distance = length of shortest vectors in Λ\Λ
  K(Λ/Λ) = The number of shortest vectors in Λ\Λ
  NoQ(α, a) = variance of effective noise n
  NOT applicable for Z[]-based LNCs
Notes: In this expression, the parameters K and d are related to the lattice partitions.

## Slide 25: Decoding error probability of LNC
  [Sun-Yuan-Huang-Shum] Consider an LNC / with  equivalent to Z[]n. The UBE of the decoding error probability for / is
  d(Λ/Λ) = length of shortest vectors in Λ\Λ
  K(Λ/Λ) = The number of shortest vectors in Λ\Λ
  N0Q(α, a) = variance of effective noise n
Notes: Now let’s move from the quantization to the decoding side of LNCs over Eisenstein integers.
Here, the shape of the sublattic Lambda’ is assumed to be isomorphic to a hypercube after possible rotation, reflection and multiplication by a scaling factor.

## Slide 26: LNC over Z[] vs over Z[i]
Z[]
  Z[] provides well-known additional shaping gain of conventional lattice codes over Z[i].
Optimal lattice packing in 2-D plane
  Under the same code rate and SNR, baseline LNC over Z[] performs slightly better than baseline LNC over Z[i].

## Slide 27: LNC over Z[] vs over Z[i]
  Two transmitters;
  A fixed channel gain
  Optimal , a are chosen.
  Baseline LNCs over Z[] are 0.5-0.6 dB better than baseline LNCs over Z[i].
Notes: SEP = Symbol error probability

## Slide 28: LNC over Z[] vs over Z[i]
  Z[] enriches candidates of finite fields for LNC designs.
    Fq can be represented by a lattice partition Z[]/Z[] if
    q = 3; or q  1 mod 6; or
      q is a square of a rational prime  2 mod 3
    Fq can be represented by a lattice partition Z[i]/Z[i] if
    q = 2; or q  1 mod 4; or
      q is a square of a rational prime  3 mod 4
  The only GF(2m) that can be represented over Z, Z[i] and Z[] are F2 = Z[i]/(1+i)Z[i] = Z/2Z and F4 = Z[]/2Z[] .
Sun-Huang-Yuan, On lattice partition based physical-layer network coding over GF(4), IEEE Comm Letters, 2013..

## Slide 29: Code design of LNC
  Theorem. Consider an LNC / over R = Z[i] or Z[]. The UBE of the decoding error probability is
  K(/) and d(/) are parameters for /.
  Construct fine lattice  from linear codes over GF(q) = R/R by complex Construction A, B, D;
  Set coarse lattice  = (R /r R)n

## Slide 30: Optimal choice of α, a
  Theorem. Consider an LNC / over R = Z[i] or Z[]. The UBE of the decoding error probability is
  K(/) and d(/) are parameters for /.
  N0(|α|2 + SNR||αh – a||2) = variance of effective noise.
  Minimum variance criterion for choosing optimal α and a.

## Slide 31: Optimal choice of a
  Theorem. Consider an LNC / over R = Z[i] or Z[]. The UBE of the decoding error probability is
  where M =
  Since M is Hermitian and positive-definite, M = LL*
lattice reduction
Notes: Where M is Hermitian and postivie-definite.
As a result, M can be further decomposed into a product of a lower triangular matrix L and its Hermitian conjugate. (This is the Cholesky decomposition).

## Slide 32: Lattice reduction
  In general, given an R-lattice  generated by a basis {v1, …, vL}, a lattice reduction algorithm aims to find another basis {u1, …, uL} s.t.
    u1 is the shortest nonzero vector in 
    u2 is the shortest vector in \u1 …
  L = 2: efficiently solved (over Z-lattice) by Guassian reduction algorithm, which is generalized to over Z[i]- and Z[]-lattices.

## Slide 33: Lattice reduction
  In general, given an R-lattice  generated by a basis {v1, …, vL}, a lattice reduction algorithm aims to find another basis {u1, …, uL} s.t.
    u1 is the shortest nonzero vector in 
    u2 is the shortest vector in \u1 …
  L > 2: No known efficient algorithm for exact optimal solutions;
  LLL algorithm is the most popular approximate one.

## Slide 34: Summary
  Via lattice partition structure embedded in C,
  finite field arithmetic can be represented over C, and thus modulation and coding can be reconciled for design of reliable PNC over a finite fields.
  information theoretical perspective,
    in TWRC, the capacity approached within 1/2 bits.
    in MARC, a lower bound on the achievable computation rate.
  practical design perspective, algebraic frameworks over both Z[i] or Z[] are developed
    UBE of decoding error probability.
    Design criteria for /, opt, aopt.

## Slide 35
Thank you.